## Slide 1
Android Automotive
HVAC Automation
Vehicle HAL Testing with Robot Framework & ADB
Robot Framework
Android Automotive
VHAL
ADB
Protobuf

## Slide 2
What Is This Project?
Goal
Automatically test whether a car's
climate control system works —
without a human pressing buttons.
What it tests:
AC On / Off
Fan Speed (0–7)
Temperature (16–32°C)
Dual Zone Mode
HVAC Power
How It Works
Robot Framework
reads .robot test files
▼
Python Keywords
call ADB commands
▼
ADB Shell
talks to Android car OS
▼
VHAL
controls car hardware

## Slide 3
What is VHAL?
Vehicle Hardware Abstraction Layer
VHAL is the translator between Android software and physical car hardware.
Every controllable car feature is a VHAL Property with a numeric ID. To turn on the AC, software tells VHAL: "set property 354419973 to 1."
Android Apps & Services
▼
VHAL ← translator layer
▼
Physical Car Hardware
HVAC Property IDs used in this project:
Property
ID
Type
HVAC Power
354419984
Boolean
AC On/Off
354419973
Boolean
Fan Speed
356517120
Integer (0–7)
Temperature Set
358614275
Float (16–32°C)
Dual Mode
354419977
Boolean

## Slide 4
What is ADB?
Android Debug Bridge
ADB is a command-line tool that lets your laptop send commands to an Android device. In this project, that device is a car's computer (head unit) or an Android Automotive emulator running on a PC.
Command Flow:
Laptop
(Python)
→
ADB
→
Android
Car OS
→
VHAL
Daemon
→
Car
Hardware
$ adb shell cmd car_service set-property-value 356517120 1 5
# Sets fan speed (property 356517120) to level 5 on the car
$ adb shell cmd car_service get-property-value 356517120 1 → Value: 5

## Slide 5
What is Robot Framework?
Keyword-driven test automation with human-readable test files
climate.robot
*** Settings ***
Library climate_keywords.py
*** Test Cases ***
Verify Fan Speed 5
Set Fan Speed 5
Sleep 1s
${speed}= Get Fan Speed
Should Be Equal As Integers
... ${speed} 5
Plain English Tests
Test cases are written like instructions, not code. QA engineers who don't know Python can read and write them.
Keywords = Python Functions
Words like "Set Fan Speed" map directly to Python functions in climate_keywords.py
Auto-Generated Reports
Robot Framework produces log.html and report.html showing which tests passed or failed, with timing and logs.

## Slide 6
Project Structure
automation/
├── tests/
│ ├── climate.robot
│ └── regression.robot
├── keywords/
│ ├── climate_keywords.py
│ ├── vehicle_properties.py
│ ├── validators.py
│ └── utils.py
├── config/
│ └── climate_config.json
├── vhal_emulator.py
└── VehicleHalProto_pb2.py
climate.robot
Individual feature tests — one test case per climate function.
regression.robot
Full pipeline smoke test — all functions in one test case.
climate_keywords.py
Core automation logic. Python functions that issue ADB commands to the car.
vehicle_properties.py
Named constants for VHAL property IDs. Prevents magic numbers.
validators.py
Input range checks — fan speed 0–7, temperature 16–32°C.
climate_config.json
Hardware limits as JSON — the source of truth for valid ranges.

## Slide 7
End-to-End Execution Flow
What happens when you run: robot tests/climate.robot
1
robot tests/
climate.robot
Robot Framework
starts
→
2
Reads test case
"Verify Fan Speed"
Finds keyword in
climate_keywords.py
→
3
set_fan_speed(5)
Python function
builds ADB command
→
4
adb shell cmd
car_service …
subprocess.run()
executes it
→
5
Android VHAL
Sets fan to 5
Hardware responds
→
6
get_fan_speed()
returns 5
Regex parses
"Value: 5"
→
7
PASS ✓
log.html created
Robot Framework
records result
run_adb() — Error Handling
ADB sometimes returns exit code 0 ("success") even when something went wrong. So the code checks three conditions:
①
returncode != 0
command itself failed
②
"no devices/emulators found"
no Android device connected via ADB
③
"Cannot set a property"
VHAL rejected the value

## Slide 8
Keywords Deep Dive
climate_keywords.py
Main keyword library
set_hvac_power(value)
set_ac(value)
set_fan_speed(speed)
get_fan_speed()
set_temperature(temp)
set_dual_mode(value)
Each function builds and runs an ADB command. Booleans cast to 1/0 for VHAL protocol.
vehicle_properties.py
Named constants
HVAC_POWER_ON = 356517120
HVAC_FAN_SPEED = 356517121
HVAC_AC_ON = 356517137
HVAC_TEMPERATURE_SET
DRIVER_AREA = 1
PASSENGER_AREA = 2
Centralises all VHAL property IDs. Change once → fixes everywhere.
validators.py
Input guard checks
validate_fan_speed(v)
→ 0 ≤ v ≤ 7
validate_temperature(v)
→ 16 ≤ v ≤ 32
validate_boolean(v)
→ must be True/False
Catches bad values before they reach the car. Currently defined but not yet wired in.

## Slide 9
VHAL Emulator & Protobuf
The lower-level communication path (not used by the main tests)
ADB Shell Approach (used by tests)
✓ Simple setup — no port forwarding
✓ Human-readable text output
✓ Easy to debug in terminal
✓ Good for functional testing
Code:
cmd = "adb shell cmd car_service"
subprocess.run(cmd)
VHAL Emulator (advanced / prototype)
Direct TCP socket to VHAL daemon
Uses Protocol Buffers (binary format)
Generated file: VehicleHalProto_pb2.py
Faster for bulk messaging
Requires adb forward for port setup
Code:
v = Vhal(VehicleHalProto_pb2)
v.setProperty(FAN_SPEED, 1, 5)
reply = v.rxMsg()
VS

## Slide 10
Test Results & Reports
Test Cases (from climate.robot)
PASS
Enable HVAC Power
Sets power on, waits 2s
PASS
Enable AC
Turns on compressor, waits 1s
PASS
Verify Fan Speed 5
Sets + reads back + asserts
PASS
Set Temperature To 22
Sets 22°C, waits 1s
PASS
Enable Dual Mode
Activates dual zones
Auto-Generated Output Files
report.html
Dashboard summary — pass/fail counts, total time, statistics. Open in a browser for an overview.
log.html
Detailed drill-down — every keyword called, every ADB command run, every value returned.
output.xml
Machine-readable raw results — used for CI/CD integration or post-processing.

## Slide 11
Key Design Decisions
Why Robot Framework?
QA engineers who aren't Python developers can read and write .robot test files. Tests look like plain English instructions.
Why ADB shell commands (not VHAL socket)?
Simpler setup — no port forwarding, no protobuf encoding, human-readable output. Ideal for functional testing where timing isn't critical.
Why vehicle_properties.py?
VHAL IDs are opaque numbers (e.g. 356517120). Naming them as constants makes code readable and lets you change a value in one place.
What's currently incomplete?
validators.py is defined but not yet called inside climate_keywords.py. Invalid inputs (e.g. fan speed 10) would still be sent to the car without pre-validation.

## Slide 12
Summary
Purpose
Automated testing of Android Automotive climate control — replaces manual button-pressing in a car.
VHAL
Translator between Android software and car hardware. Every feature is a numbered property (e.g. fan speed = 356517120).
ADB
The bridge between laptop and car OS. Commands like adb shell cmd car_service control and read VHAL properties.
Robot Framework
Reads plain-English .robot test files and calls Python keyword functions. Generates HTML reports automatically.
Keywords
Python functions in climate_keywords.py that build and run ADB commands, parse output, and raise errors on failure.
Output
log.html, report.html and output.xml are auto-generated, showing pass/fail status for every test case.